## Slide 1
Gasification Of Any Waste Train:
Agriculture, MSW, Sludge & Bio-Solids, Construction Waste, etc.
RELIANCE ENERGY SYSTEM

## Slide 2: Agenda
Background
Process Fundamentals
Commercial Status
Energy Balances
Gasification Relative to Today’s Issues
Summary
2

## Slide 3: Background – History of Gasification
Charcoal formation (pyrolysis)
  Several thousand years old
Gasification
  Large scale use on coal in the 1800’s; wood in 1900’s
  New focus → alternative feedstocks
3
EPA, U.S. (2012). Technology Assessment Report: Aqueous Sludge Gasification Technologies.

## Slide 4: Process Fundamentals
Pyrolysis Reactions
4
Carbon Feedstock
Char
Tars H2 CH4
General Steps
Drying
Combustion (oxidation)
Gasification (reduction)
Main Types of Gasifiers
Fixed bed
Rotating Fluidized bed
Heat

## Slide 5: Reaction Pathways
Combustion (Oxidation) Reactions
Gasification (Reduction) Reactions

## Slide 6: Feedstock Heating Methods
Plasma Torch (Westinghouse)
Combustion:
Char + Limited O2 → CO2 + CO + H2O + Heat
Heater Source:
FEEDSTOCK W/MOISTURE>20%
FEEDSTOCK W/ DESIRED MOISTURE CONTENT

## Slide 7: Feedstock Properties
Proximate Analysis of Various Waste Train Feedstocks
9
Parameter | MSW | Bio-Solids | Agriculture Waste | Construction Waste
Ash, % |  | 40-50 |  | 
Volatile, % |  | 40-50 |  | 
Fixed C, % |  | 5-10 |  | 
HHV, Btu/lb Sources: 1. Stamford Waste to | Energy Draft Report; 2. Gikas et al., 2 | 3000-5500 011 |  | 

## Slide 8: Syngas Properties
Energy Content of Syngas, Biogas and Natural Gas
  100-130 Btu/ft3 typical (air-blown)
  Biogas ~550 Btu/ft3
  Natural gas ~950 Btu/ft3
Primarily CO and H2
Usually highly diluted with N2
Syngas conditioning required for use in a gas engine
Thermal oxidation of syngas avoids gas cleaning
Example Syngas Composition (v/v)
Hydrogen = 9%
Carbon monoxide = 14%
Carbon dioxide = 20% Methane = 7%
Nitrogen = 50%
10

## Slide 9: Gasification vs. Incineration
Gasification
Reducing environment
Limited oxygen
Drying required as • Drying not required as pretreatment step pretreatment step
Designed to maximize • Designed to maximize
feedstock conversion to CO and H2
Incineration
feedstock conversion to CO2 and H20
Highly oxidizing environment
Excess air

## Slide 10: Biosolids Gasification Configurations
Close-Coupled Gasification
No syngas cleaning
Syngas thermally oxidized
Heat recovery and/or power generation from flue gas
Dewatering
Wet Sludge
Drying
Gasification
Syngas Utilization
Energy for Drying
Main Energy Sink
Excess Energy

## Slide 11
Dried Sludge
Gasification
Limited O2
AND /Or
External Heat
Syngas
Thermal Oxidation
Flue Gas Treatment
Stack
Excess O2
Process Heat
Metal Granules Coated
with Silica
CLOSE COUPLED GASIFICATION

## Slide 12: Process Diagram for Kopf Gasification Plant

## Slide 13: Staffing Requirements
Sanford facility staffing requirements
  6 full-time operators
  Plant manager and administrator
  Owned and operated by MaxWest
Now offering gasification equipment as capital sale
Typical installed cost in the range of $7-10M
20

## Slide 14: Syngas from “Fresh Solids”
Trials with solids from Adelanto, CA WWTP
January and June of 2010
Syngas properties
• CO = 31.5%
• H2 = 49.2%
• CH4 = 7.73%
• CO2 = 3.20%
  8.83% “unidentified gases”
Gikas et al., 2011
UHT Gasifier
Rotary Fabric Fine Screen

## Slide 15: Stamford, CT Waste to Energy Project
High electricity costs
• $0.18/kwh
  City identified need for up to 15 MW additional power
Proposed gasification system to generate electricity
  25 tpd (dry) facility
  Produce 1-3 MW of electricity from syngas
2007 - Thermal drying facility constructed
Pilot gasification facility
  Trailer mounted fixed-bed updraft gasifier (0.53 tpd)
2008 to 2009 - Full-scale trials with three vendors
  Primenergy, Nexterra, Kopf

## Slide 16: Stamford Pilot Gasifier
Gasification pilot donated to UCONN for research in March 2012…
Trailer Mounted Gasification Pilot
24
www.stamfordbiogas.com/Kappe%20Gasification%20for%20SF.pdfSimilar
Fixed-bed Updraft Reactor

## Slide 17: Stamford/Nexterra Current Status
“The public balked at the project's $40 million price tag, and the WPCA board voted to kill the venture in early 2010 after losing faith in its technical and economic feasibility.”
Read more: http://www.stamfordadvocate.com/news/article/ Waste-to-energy-remnant-donated-to-
UConn-3431002.php#ixzz2AAK4RDIv
25

## Slide 18: Energy Balance Considerations
Net Energy = Energy Outputs – Energy Inputs
Main energy outputs
  Electric power
  Heat
Main energy inputs (parasitic loads)
  Dryer
  Blowers
  Gasifier startup
  Gasifier external energy needs
    Induction heater, plasma torch, etc.
  Syngas cleanup
26
Courtesy of Huber

## Slide 19: Power Generation Options
Engine Cooling Jacket Heat Recovery
Fuel cells – not currently used with syngas
Gas turbines – require minimum heating value of 450 Btu/ft3 and pressurization of syngas
Internal combustion engines – possible
  Requires minimum heating value of ~140 Btu/ft3
  Still may need to blend with natural gas
27
Gas Engine
Engine Exhaust Heat Recovery
Blended Gas
Natural Gas (if needed)
Syngas
Electric Power

## Slide 20: Energy Required for Drying
Thermodynamics
  Typically 1,400-1,700 Btu/lb of water evaporated
Heat sources:
  Natural gas, methane, propane, electric power
Recovered heat, waste heat
Solar
Scenario
Energy Required (MMBtu/hr)
Natural Gas Cost ($/yr)
Power Cost ($/yr)
15% Solids Feed
17.4
$1,181,000
$2,006,000
20% Solids Feed
12.2
$827,000
$1,404,000
25% Solids Feed 9.0
$614,000
$1,043,000
28
Assumes 1,500 Btu/lb water evaporated, 90% dry solids product, natural gas = 1,030 Btu/cf, natural gas =$8/1000-cf, power = $0.045/kWh
For a 25 dtpd drying facility:
25 dtpd gasification + thermal oxidation system could yield
approx. 8-10 MMBtu/hr

## Slide 21: Energy Balances Presented in Literature
5 tpd two-stage gasification system (~4-6 mgd WWTP)
Energy balances NOT from actual full-scale operation
Air-Blown Gasifier 1 M2R/Pyromex Gasifier 2
M2R also presented energy balances in recent paper for a hypothetical 20 mgd WWTP (Noll, 2012)
  Claimed net electrical energy output of nearly 2:1 vs. anaerobic digestion
1. Source: US EPA, 2012; 2. Source: M2R Thermal Energy Conversion Brochure
Net output = 165 kW
Assumptions:
Syngas HHV = 190 Btu/ft3
System parasitic load = 75 kW
Biosolids dried to 90% solids
Net output = 295 kW
Assumptions:
Syngas HHV = 338 Btu/ft3
System parasitic load = 116 kW
Biosolids dried to 78% solids

## Slide 22: Energy Balances Presented in Literature
From Stamford Waste to Energy project report:
  Biosolids feed rate = 3,695 lb/hr
  Syngas production rate = 2,595 scfm
  Syngas LHV = 117 Btu/scf
  Quantity of syngas = 84,287 scf/ton-biosolids
  Cold gas efficiency = 69.4%
  Gross electric power production = 1,869 kW
  Net electric power production = 1,623 kW
Proposed facility footprint of 140’x100’
Project killed due to cost and technical feasibility

## Slide 23: Energy Balances from Operating Facilities
Kopf – Balingen plant
  Digested sludge
  Equivalent to approx. 7.2 mgd
  Original plant used solar drying
    Produced ~70 kW of electric power
      15 kW needed for parasitic loads
      ~55 kW net
    Produced ~140 kW of thermal energy
      Used to heat digesters at the WWTP
  Rebuilt in 2006 – added belt dryer
    Most of the gas now used for heating the belt dryer
31
Courtesy of Kopf

## Slide 24
MaxWest facility in Sanford, FL
Main goal is an energy-neutral system
  Current input to dryer is 16% solids
  Needs to be dried to 90% solids
  Current system requires natural gas supplement for dryer
According to MaxWest, achieving energy-neutral requires:
  23-25% solids feed depending on ratio of primary/secondary sludge
Energy Balances from Operating Facilities

## Slide 25: Economics of Two-Stage Sludge Gasification
Economics largely dependent on electricity cost
  Renewable energy tariff
Case
National Average Wholesale Electricity Rate
New England Average Industrial Electricity Rate + RE Tariff ($0.0435/kWh)
Electricity Cost, $/kWh
$0.042
$0.093
Tipping Fee, $/DT
$70
$70
Annual Operating Revenue, $
$41,624
$61,742
Annual Operating Cost, $
($36,995)
($41,551)
Capital Costs, $
($269,815)
($269,815)
CAPEX per kW, $/kW
$4,652
$4,652
Payback Years 21
Costs presented in USD per dry ton per day operating capacity; source: US EPA, 2012
7

## Slide 26: Air Emissions Regulatory Requirements
Currently no specific EPA regulations
  Case by case basis
  May be classified as incinerators
Criteria air pollutants
  Sulfur oxides (SOx)
  Carbon monoxide (CO)
  Nitrogen oxides (NOx)
  Particulate Matter (PM)
Hazardous air pollutants
  Hydrogen chloride (HCl)
  Dioxins and furans (chlorinated organics)

## Slide 27: Air Emissions Data
Emission Limits in 40 CFR Part 60 – Final Rule for SSIs
Source: US EPA, 2012
Source: data provided by MaxWest
Pollutant | Units | Existing FB SSIs | New FB SSIs | MaxWest Gen #1 1 | MaxWest Gen #2 2
Cadmium (Cd) | mg/dscm | 0.0016 | 0.0011 | 0.0000723 | -
Carbon Monoxide (CO) | ppmvd | 64 | 27 | 7.87 | 16.1
Hydrogen Chloride (HCl) | ppmvd | 0.51 | 0.24 | 1.8 | 0.321
Mercury (Hg) | mg/dscm | 0.037 | 0.0010 | 0.00798 | -
Oxides of Nitrogen (NOx) | ppmvd | 150 | 30 | 432.17 | 15.4
Lead (Pb) | mg/dscm | 0.0074 | 0.00062 | 0.000819 | -
Dioxins/Furans | ng/dscm | 0.10 | 0.0044 | 0.0285 | -
Particulate Matter (PM) | mg/dscm | 18 | 9.6 | 9.6 | 8.23
Sulfur Dioxide (SO2) | ppmvd | 15 | 5.3 | 4.17 | 0.0

## Slide 28: Gasification Relative to Today’s Issues
Energy
? Potential for energy generation (depends on syngas quality)
- Drying required as a pretreatment step
- Heat recovery mostly used for drying
Emissions
+ Reduced relative to incineration
+ Lower air requirements
+ Reducing environment
Regrowth/Reactivation
+ Pathogens destroyed
+ No biosolids to dispose of
Resource Recovery
+ POTENTIAL P recovery from ash
No N recovery
Process Reliability
Four full-scale installations worldwide
One full-scale installation in North America

## Slide 29: Be Aware of the Process Cycle History…
Incineration Second Generation
Biosolids Drying First Demo
Thermal Hydrolysis
Biosolids Gasification
SCWO
Time
Development / No. Installed
First Pilot
First Applications
Third Generation, Mature Technology
Anaerobic Digestion

## Slide 30
Questions?
Thank You!
38
Courtesy of Kopf
Courtesy of Nexterra

## Slide 31: References
Judex, J., Gaiffi, M., Burgbacher, H. (2012). Gasification of dried sewage sludge: Status of the demonstration and the pilot plant. Waste Management, 32 (4), 719-723.
Gikas, P., Noll, S., Stedman, K. “Gasification of Primary Fine-Screened Solids for Energy Production,” Eurasia Waste Management Symposium, Halic Congress Center, Istanbul, Turkey, November 14-16, 2011.
Mountouris, A., Voutsas, E., Tassios, D. (2008). Plasma gasification of sewage sludge: Process development and energy optimization. Energy Conversion and Management , 49 (8), 2264-2271.
EPA, U.S. (2012). Technology Assessment Report: Aqueous Sludge Gasification Technologies. U.S. Environmental Protection Agency.
Noll, S. (2012). A Net Energy Comparison of Anaerobic Digestion vs. Ultra-High Temperature Gasification to Achieve Zero Energy, WEF Residuals and Biosolids 2012.
Li-ping, X., Tao, L., Jian-dong, G., Xue-ning, F., Xia, W., Yuan-guang, J. (2010). Effect of moisture content in sewage sludge on air gasification. J Fuel Chem Technol , 38 (5), 615-620.
39