## Slide 1
1. Provide better power/ground distribution
Increased static capacitance due to thinner core
Lower power/ground plane transient impedance due to larger capacitance
Electrical Advantages of Thin Core Substrate
Core Permittivity
Plane Area
Core Thickness
Static Capacitance
Thin core vs. conventional core electrical performance comparison
Notes: Decreased operation voltage and increased power demands require increased current to run the whole system, which demands a low impedance value for power/ground distribution network.

## Slide 2
Electrical Advantages of Thin Core Substrate
2. Improved signal integrity
Smaller parasitic inductance due to shorter via length (minimize the impedance discontinuity)
Reduced power/ground inductance due to shorter via length (minimize the SSN)
Number of Switches
Parasitic Inductance
Rate of Current Change
Induced Voltage
Thin core vs. conventional core electrical performance comparison
Notes: Superior wiring density due to smaller via diameters and finer design rules makes it possible for packing a shrunk die in a smaller package, or retaining the package size while allocating more I/Os for power/ground for even lower parasitic inductance higher current handling capability and better heat dissipation.

## Slide 3
3. Other benefits
Increasing ground to signal I/O ratios for improved signal integrity
Using stripline structure for lower crosstalk
Both cases help to mitigate EMI
Electrical Advantages of Thin Core Substrate
Extra solid plane in the stripline structure constrains electrical field within signal trace and solid planes resulting in lower crosstalk and EMI
a) Microstrip
b) Stripline
Dielectric
W
W
S
H
t
t
Dielectric
W
W
S
H
t
H
Notes: Possible to provide a thin profile package solution. If profile maintained, then prossible to incorporate more solid plane as power/ground plane.