## Slide 1
5.Linear Superposition Principle
(For Experiments)
This technique is extremely useful for effective thermal resistance characterization of thermal models of Multi-Chip modules, hybrid device,or devices having multiple heat sources. It can also be used to verify the computer models.
Main Concept (superposition principle) is extracted from Analysis Tec Inc. (www.analysistech.com) and from the reference articles.
Thermal evaluation of stacked die packages

## Slide 2
Linear conductor bar with uniform heat sources
Conductor bar
Insulation
Specification:
Insulated conductor bar
No insulation at the ends.
Both ends are at fixed temperature
Single heat source is operating
1
Heat source @ “2”-Active
2
T12
T22
0
L
To
To
Temperature profile for point-heat-sources in an insulated bar of length ‘L’ with ends at fixed temperature
1
2
Internally embedded Heat sources
Infinite Heat Sink at both ends at To
Thermal evaluation of stacked die packages

## Slide 3
This superposition solution can be similarly expressed in terms of thermal resistances:
R11=(T11-To)/Q1
  Thermal resistance manipulations can be cast in matrix form for convenience in our case of two heat sources:
  R11 R12 Q1 T1-To
  R21 R22 Q2 T2-To
        R Q = T
*
=
*
This will yield the required Junction
temperatures of the chips
Thermal evaluation of stacked die packages

## Slide 4
7. References
1. B. Guenin, "The Many Flavors of Ball Grid Array Packages," Electronics Cooling, Vol. 8., No. 1, February, 2002, pp. 32-40.
2. Bruce M. Guenin, Ph.D., Associate Editor, Sun Microsystems
"Thermal Calculations for Multi-chip Modules” Nov 2002 ," Electronics Cooling,
3. All JEDEC thermal standards can be found at the JEDEC web site, www.jedec.org, in the following series: EIA/JESD51-X.
4. B. Guenin, "1-Dimensional Heat Flow," Electronics Cooling, Vol. 3., No. 3, September, 1997, p. 15
5 Wen-Hwa Chen, “An Effective methodology for Thermal Characterization of Electronic Packaging," IEEE Trans. Comp., Packaging, Technol., Vol. 26, No. 1, March 2003, pp. 222-232.
6 B. Zahn, "Steady State Thermal Characterization of Multiple Output Devices Using Linear Superposition Theory and a Non-Linear Matrix Multiplier," Proceedings SEMI-THERM XIV Conference, March, 1998, pp. 39-46.
Cond…
Thermal evaluation of stacked die packages

## Slide 5
*Thanks*
Thermal evaluation of stacked die packages